## Slide 1
Orbit comparison for ERS-1 mission between GFZ and REAPER
The GFZ orbit is referred to as GFZ in the following study
The REAPER orbit is referred to as SL_cci
Lionel Zawadzki, Michael Ablain (CLS)

## Slide 2
Introduction:
We will observe and analyse the impact of the precise orbit computed by GFZ for climate applications. It will be referred to as “GFZ”.
We will compare this orbit with the reference one in SL_cci products, computed by REAPER project. It will be referred to as “SL_cci”.
In order to determine the impact of the GFZ orbit in terms of climate applications and temporal scales, we will try in this study to indicate for each impact detected if it’s a positive (+) or a negative (-) impact :
Orbit comparison for ERS-1 mission
No impact detected
Low impact
Significant impact

## Slide 3
ERS-1 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Global Mean Sea Level
Significant impact detected on Global Mean Sea Level trend
0.29mm/yr trend difference on the Global MSL
Temporal evolution of SLA mean calculated globally.

## Slide 4
ERS-1 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Global Mean Sea Level
No impact detected on Inter annual Signals
The figure below shows the mean difference between the two orbits calculated globally by cycle.

## Slide 5
ERS-1 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Global Mean Sea Level
No impact detected on Periodic Signals

## Slide 6
ERS-1 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | -
Significant impact detected on a short temporal scale (signals < 2 months):
Crossovers Variance Differences are generally positive (see figures on next slide) between 1 and 9 cm²: This means that the new GFZ orbit shows a strong degradation by comparison to the SL_cci orbit.
The map of SSH crossovers Variance Differences shows that these degradations are global.
Mesoscale

## Slide 7
Mesoscale
Map of Variance differences of Sea Surface Height at crossovers between the GFZ and SL_cci orbits (over all the period):
Significant degradation (4 cm²) In the West Pacific and Atlantic oceans; 2cm² in the East Pacific and Indian oceans.
Temporal evolution of Variance differences of Sea Surface Height at crossovers between two Orbits:
Degradation (between 0 and 2cm²) with GFZ.

## Slide 8
ERS-1 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Significant impact detected on Regional Mean Sea Level
We observe a strong impact (~2 mm/yr) on the regional trends. It is positive in the Atlantic and West Pacific Oceans; and negative in the Indian and East Pacific Oceans. It is not possible to determine which orbit is better.
Regional Mean Sea Level

## Slide 9
Regional Mean Sea Level
Map of Sea Level Anomaly differences between two Orbits (over all the period)

## Slide 10
ERS-1 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Amplitudes differences reach 3mm or -3mm for annual and semi-annual signal (see figures on next slide).
These differences are small and it is not possible to determine which orbit is the best one for theses scales.
However, the impact on the phases is significant as it reaches 20° (about 20 days of phase shift)
Regional Mean Sea Level
Significant impact detected on Annual and Semi-Annual Signals

## Slide 11
Regional Mean Sea Level
Map of Sea Level Anomaly differences amplitude for annual signal
Map of Sea Level Anomaly differences amplitude for semi-annual signal
SLA with GFZ amplitude – SLA with SL_cci amplitude : semi-annual signal
SLA with GFZ amplitude – SLA with SL_cci amplitude : annual signal

## Slide 12
Regional Mean Sea Level
Map of Sea Level Anomaly differences phase for annual signal.
Map of Sea Level Anomaly differences phase for semi-annual signal.
To be noted a phase value equal to 30° corresponds to a period of one month
SLA with GFZ phase – SLA with SL_cci phase : semi-annual signal
SLA with GFZ phase – SLA with SL_cci phase: annual signal

## Slide 13
Map of Mean differences between GFZ and SL_cci (whole ERS-1 period)
On this map we observe a difference up to 1 cm in the Indian and West Pacific Oceans. The differences between the orbits become negative, down to -2mm in the East Pacific Ocean and East Atlantic Oceans
Map of Standard deviation of the differences between GFZ and SL_cci (whole ERS-1 period)
On this map we observe strong differences (~1.5cm) globally except in the East Pacific and Indian Oceans.
Regional statistics between orbits

## Slide 14
To conclude:
The orbit computed by GFZ shows:
performances degraded at crossovers by comparison to SL_cci.
significant impact at regional and global scales, however, it is not possible to determine which orbit is better.
These results have to be moderated by the ERS-1 period length, too short
ERS-1 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Periodic Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | -
Orbits comparison for ERS-1 mission