## Slide 1
Orbit comparison for Envisat mission between GFZ and CNES (POE-D)
The GFZ orbit is referred to as GFZ in the following study
The CNES orbit is referred to as SL_cci
Lionel Zawadzki, Michael Ablain (CLS)

## Slide 2
Introduction:
We will observe and analyse the impact of the precise orbit computed by GFZ for climate applications. It will be referred to as “GFZ”.
We will compare this orbit with the reference one in SL_cci products, computed by CNES (POE-C). It will be referred to as “SL_cci”.
In order to determine the impact of the GFZ orbit in terms of climate applications and temporal scales, we will try in this study to indicate for each impact detected if it’s a positive (+) or a negative (-) impact :
Orbit comparison for Envisat mission
No impact detected
Low impact
Significant impact

## Slide 3
Envisat |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Global Mean Sea Level
No impact detected on Global Mean Sea Level trend
0.03mm/yr trend difference on the Global MSL
Temporal evolution of SLA mean calculated globally.

## Slide 4
Envisat |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Global Mean Sea Level
Low impact detected on Inter annual Signals
The figure below shows the mean difference between the two orbits calculated globally by cycle.

## Slide 5
Envisat |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Global Mean Sea Level
No impact detected on Periodic Signals

## Slide 6
Envisat |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Low impact detected on a short temporal scale (signals < 2 months):
Crossovers Variance Differences are either positive or negative (see figures on next slide) between -0.50 and +0.50 cm²: This means that the new GFZ orbit has a significant impact by comparison to the SL_cci orbit but it is not possible to assess which one is better.
The map of SSH crossovers Variance Differences shows that the impact may be positive or negative without any specific area detected.
Mesoscale

## Slide 7
Mesoscale
Map of Variance differences of Sea Surface Height at crossovers between the GFZ and SL_cci orbits (over all the period):
Significant impact globally (between -1cm² and +1cm²).
Temporal evolution of Variance differences of Sea Surface Height at crossovers between two Orbits:
Difference between -0.5cm² and +0.5cm²

## Slide 8
Envisat |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Low impact detected on Regional Mean Sea Level
We observe a strong impact (~0.5 mm/yr) on the regional trends. It is positive in the Atlantic and East Pacific ; and negative in the Indian and West Pacific Oceans. It is not possible to determine which orbit is better.
Regional Mean Sea Level

## Slide 9
Regional Mean Sea Level
Map of Sea Level Anomaly differences between two Orbits (over all the period)

## Slide 10
Envisat |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Amplitudes differences reach 3mm or -3mm for annual and semi-annual signal (see figures on next slide).
These differences are small and it is not possible to determine which orbit is the best one for theses scales.
However, the impact on the phases is significant as it reaches 20° (about 20 days of phase shift)
Regional Mean Sea Level
Low impact detected on Annual and Semi-Annual Signals

## Slide 11
Regional Mean Sea Level
Map of Sea Level Anomaly differences amplitude for annual signal
Map of Sea Level Anomaly differences amplitude for semi-annual signal
SLA with GFZ amplitude – SLA with SL_cci amplitude : semi-annual signal
SLA with GFZ amplitude – SLA with SL_cci amplitude : annual signal

## Slide 12
Regional Mean Sea Level
Map of Sea Level Anomaly differences phase for annual signal.
Map of Sea Level Anomaly differences phase for semi-annual signal.
To be noted a phase value equal to 30° corresponds to a period of one month
SLA with GFZ phase – SLA with SL_cci phase : semi-annual signal
SLA with GFZ phase – SLA with SL_cci phase: annual signal

## Slide 13
Map of Mean differences between GFZ and SL_cci (whole Envisat period)
On this map we observe differences up to 5mm at high latitudes and down to -2mm at low latitudes.
Map of Standard deviation of the differences between GFZ and SL_cci (whole Envisat period)
On this map we observe strong differences (between 0.7 and 1cm)
Regional statistics between orbits

## Slide 14
To conclude:
The orbit computed by GFZ shows equivalent performances by comparison to SL_cci
Low impacts are detected on the long-term evolutions at regional scale and on the mesoscale and periodic signals: we are not able to determine which solutions is the best one.
Envisat |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Periodic Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Orbits comparison for Envisat mission