## Slide 1
Orbit comparison for Jason-1 mission between GFZ and CNES (GDR-D)
The GFZ orbit is referred to as GFZ in the following study
The CNES orbit is referred to as SL_cci
Lionel Zawadzki, Michael Ablain (CLS)

## Slide 2
Introduction:
We will observe and analyse the impact of the precise orbit computed by GFZ for climate applications. It will be referred to as “GFZ”.
We will compare this orbit with the reference one in SL_cci products, computed by CNES (GDR-D). It will be referred to as “SL_cci”.
In order to determine the impact of the GFZ orbit in terms of climate applications and temporal scales, we will try in this study to indicate for each impact detected if it’s a positive (+) or a negative (-) impact :
Orbit comparison for Jason-1 mission
No impact detected
Low impact
Significant impact

## Slide 3
Jason-1 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | ---
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Global Mean Sea Level
Low impact detected on Global Mean Sea Level trend
0.27mm/yr trend difference on the Global MSL but mainly due to last cycles where strong abnormal signals are detected
error on GFZ orbit solutions
Temporal evolution of SLA mean calculated globally.

## Slide 4
Jason-1 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | -
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Global Mean Sea Level
Low impact detected on Inter annual Signals
The figure below shows the mean difference between the two orbits calculated globally by cycle.
It’s not easy to determine inter-annual signals due to the wrong signals at the beginning and at the end of the period (errors on the GFZ solution)

## Slide 5
Jason-1 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | - (60 days)
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Global Mean Sea Level
Significant impact detected on Periodic Signals
The impact on annual and semi-annual signals is low (about 0.5mm)
> 0.5 mm impact on 58.77-day signal. This signal is an error on GFZ orbit solution.

## Slide 6
Global Mean Sea Level
Upper left panel: Periodograms of SLA around 1 year
Lower left panel: Periodograms of SLA between 0-1 year
Lower right panel: Periodograms of SLA around 58.77-day

## Slide 7
Jason-1 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | -
Significant impact detected on a short temporal scale (signals < 2 months):
Crossovers Variance Differences are generally positive (see figures on next slide) between 0 and 4 cm²: This means that the new GFZ orbit shows a strong degradation by comparison to the SL_cci orbit.
The map of SSH crossovers Variance Differences shows that these degradations are everywhere (global scale).
Mesoscale

## Slide 8
Mesoscale
Map of Variance differences of Sea Surface Height at crossovers between the GFZ and SL_cci orbits (over all the period):
Significant degradation (4 cm²) at latitudes >±30° and 2cm² at lower latitudes.
Temporal evolution of Variance differences of Sea Surface Height at crossovers between two Orbits:
Degradation (between 2 and 4cm²) with GFZ

## Slide 9
Jason-1 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Significant impact detected on Regional Mean Sea Level
We observe a strong impact (>1 mm/yr) on the regional trends. It is positive in the Atlantic and the Indian oceans; and negative elsewhere.
Comparison with CNES GDR-E orbit solutions could be foreseen
Regional Mean Sea Level

## Slide 10
Regional Mean Sea Level
Map of Sea Level Anomaly differences between two Orbits (over all the period)

## Slide 11
Jason-1 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | 
 | Inter annual signals (> 1 year) | 
 | Annual and semi-annual Signals | 
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | 
Amplitudes differences reach 3mm or -3mm for annual and semi-annual signal (see figures on next slide).
These differences are small and it is not possible to determine which orbit is the best one for theses scales.
However, the impact on the phases is significant as it reaches 20° (about 20 days of phase shift)
Regional Mean Sea Level
Low impact detected on Annual and Semi-Annual Signals

## Slide 12
Regional Mean Sea Level
Map of Sea Level Anomaly differences amplitude for annual signal
Map of Sea Level Anomaly differences amplitude for semi-annual signal
SLA with GFZ amplitude – SLA with SL_cci amplitude : semi-annual signal
SLA with GFZ amplitude – SLA with SL_cci amplitude : annual signal

## Slide 13
Regional Mean Sea Level
Map of Sea Level Anomaly differences phase for annual signal.
Map of Sea Level Anomaly differences phase for semi-annual signal.
To be noted a phase value equal to 30° corresponds to a period of one month
SLA with GFZ phase – SLA with SL_cci phase : semi-annual signal
SLA with GFZ phase – SLA with SL_cci phase: annual signal

## Slide 14
Map of Mean differences between GFZ and SL_cci (whole Jason-1 period)
On this map we observe a difference up to 5 mm over 50° latitude and in Indian Ocean. The differences between the orbits become negative, down to -5mm in the Pacific Ocean.
Map of Standard deviation of the differences between GFZ and SL_cci (whole Jason-1 period)
On this map we observe strong differences (~1cm) globally
Regional statistics between orbits

## Slide 15
To conclude:
The orbit computed by GFZ shows performances strongly degraded by comparison to SL_cci (CNES GDR-D).
The main impacts are on the long-term evolutions at regional scale and on the mesoscale and periodic signals:.
  Scores at crossovers show, SL_cci is better for the mesoscale signal over Jason-1 Period.
  The 58-day (strong homogenous signal over all the period) signal in GFZ orbit may be considered as an error
  For the regional trends, more investigations are necessary to show if it is an improvement or not
Jason-1 |  | 
Climate Applications | Temporal Scales | Round Robin Data Package (RRDP)
 |  | GFZ Versus SL_cci
Global Mean Sea Level | Long-term evolution (trend) | -
 | Inter annual signals (> 1 year) | -
 | Periodic Signals | - (60 days)
Regional Mean Sea Level | Long-term evolution (trend) | 
 | Annual and semi-annual Signals | 
Mesoscale | Signals < 2 months | -
Orbits comparison for Jason-1 mission